## Slide 1: Thesis Update
02 March 2026
Connor Emmons

## Slide 2: Hamiltonian vs Jacobi Constant
Jacobi
Hamiltonian

## Slide 3: Changing Mesh Size
Attempted to change mesh to segments, points = 100, 10
No good

## Slide 4: Iterative Solution
First generate the original good orbit, then use the state and time from that orbit as the initial guess for a second solution with a mesh of 100, 10
Jacobi constant got worse, but still within good ranges
  Shapes of Jacobi and Hamiltonian match for this case
Jacobi
Hamiltonian
(difference to mean)

## Slide 5: Iterative Solution Refined
For the second solution, in addition to adjusting the mesh, remove the bounds on the final time (reset to 0, infinity)
This orbit was off of the period stated in the paper by ~1.7% (~18 hours)
  Hamiltonian getting better
The original solution takes ~20 seconds to run, the second solution takes ~5 seconds to run
(difference to mean)

## Slide 6: Attempted Relaxation of Tolerance
Attempted to relax ipopt tol to 1e-16 from 1e-100 to reduce run times
  No good

## Slide 7: Attempted New Mesh with No tf Bounds
Remove final time bounds and try one solution but with a mesh of 100, 10
  Orbit is no good, but Jacobi and Hamiltonian agree
(difference to mean)

## Slide 8: Attempted New Mesh with Loose tf Bounds
Reinstated bounds, but gave an interval of +- 5 days (good orbits are generated with 0.95 difference)
  Solution still bad, but Jacobi and Hamiltonian still match-ish
(difference to mean)

## Slide 9: Discussion
Jacobi and Hamiltonian agreeance seems dependent on the mesh used
  100, 10 gives good agreeance, but 30, 30 does not
  Testing with different bounds shows that big changes on one graph reflect big changes in the other, but the magnitude and direction are not necessarily the same
  Discuss recent results
    Jacobi value vs Hamil offset, deviation vs Hamil deviation
Not sure how to feel about iterative solution
  Hamiltonian and Jacobi in much closer agreeance (good) but period is worse (bad)
  Could come down to how accurate the period given in the paper is and/or how much to trust other people’s work

## Slide 10: Future Work
Implement in 3D
More testing of Jacobi vs Hamiltonian
  Which one is a better predictor of a “good” orbit?
  Should they agree?
  Might be necessary to evaluate orbit generation in 3D
Once 3D is implemented, try to find off-axis cyclers
At some point, have to model other cyclers for completeness